## Slide 1: Alternative Interdomain Routing Schemes
Colin Scott
Notes: Put affiliations in parentheses
Add sponsors: Google, Cisco, NSF

## Slide 2: Normal Discussion

## Slide 3: Today’s Discussion
Notes: Maybe we can make it like a choose your own adventure

## Slide 4
Notes: Ok, this is annoying

## Slide 5
Notes: But we’d like to do remote health monitoring … this is plain dangerous.

## Slide 6: How common are these outages?
86% of outages are less than 5 minutes
Long outages account for 90% of the downtime
Portion of outages
Portion of total downtime
Monitor network outages from Amazon’s EC2
2 million outages in two months
Notes: Most outages are short – good!
But those long ones – responsible for most of the downtime

## Slide 7: Internet Routing
A goal of the Internet is global reachability
But, BGP fails to achieve this goal
  Physical paths exist, but not BGP paths
  10-15% of BGP updates cause loops and blackholes
  90% of all packet losses on the Internet due to loops
Notes: Global reachability == every address is reachable from every other address
BGP, the routing protocol of the internet fails to reach this goal.
i.e. though physical paths exist, packets don’t make it to the destination
Simulation results showed that a single link failure can cause a significant portion
of the Internet to experience transient disconnectivity
Lots of studies on BGP

## Slide 8: Example
5: 4-5
5: 3-4-5
5: 1-5
5: 4-5
5: 2-4-5
2
3
4
5
1
Destination
Notes: Routing table is shown above the Ases 2, 3, 6
The path in yellow is the selected best path
Remaining paths are listed in order of preference

## Slide 9: Link Failure
5: 4-5
5: 3-4-5
5: 1-5
5: 4-5
5: 2-4-5
5:4-5
Link 4-5 fails
AS4 withdraws path
from upstream ASes
2
3
4
5
1
Notes: Routing table is shown above the Ases 2, 3, 6
The path in yellow is the selected best path
Remaining paths are listed in order of preference

## Slide 10: Lack of Consistency
The underlying cause of all these problems is inconsistent global state
  Link failures
  Traffic engineering
  Scheduled Maintenance
  Link coming up
Protocol behavior complex, unpredictable
No indicator of when system converged to consistent state
Notes: Routers by design operate on inconsistent distributed state
Clearly, inconsistency is bad

## Slide 11: Consensus Routing
Lesson from distributed system design:
  De-couple safety and liveness
Safety: Forwarding tables are always consistent and policy compliant
Liveness: Routing system adapts to failures quickly
Notes: We borrow an old lesson in dist system design
In the context of internet routing: safety defined as ‘ forwarding tables consistent, policy compliant. required for correctness
Liveness: routing system adapts to failures quickly, and maintains availability
Different mechanisms appropriate for each

## Slide 12: Safety
How do we ensure consistency?
  Apply updates only after they have reached everyone
  Apply updates at the same time everywhere
Notes: 2 simple rules: apply updates only after they have reached everyone
apply updates at the same time everywhere
With these two principles in mind, the mechanism follows in a rather straightforward manner
Next few slides will be chunking through the mechanism

## Slide 13: Deciding on Routes
Centralized Consensus Algorithm (PAXOS)
Notes: Tier 1 providers run the consensus nodes

## Slide 14: Atomic Commit
One set of routes per “epoch”
Routers only apply routes after all other routers have access to those policies
Mark each packet with a single epoch

## Slide 15: Liveness
After link failure, new path announced
Need to wait till path reaches everyone
  Takes time!
Solution: Dynamically re-route around the failed link
  use existing techniques
    Pre-computed backup paths
    Detour routing
Notes: We’ve looked at how we can provide safety.
Let us now consider a mechanism for liveness …
As defined earlier: liveness corresponds to ‘system adapting to changes quickly and maintaining availability’
To maintain consistency, … need to wait
This delay can lead to unavailability
This ensures that while we are waiting for the system to converge to a stable state, we don’t have long periods of disconnectivity
Illustration of the operational difference between BGP and consensus routing

## Slide 16: Conclusions
BGP’s transient problems are due to inconsistent global state
Consensus routing enables consistent routing state with opaque policies
  key technique: separation of safety and liveness
  Maintain consistency whenever possible.
  Only route on inconsistent information when necessary.
Notes: BGP’s transient problems are due to inconsistent global state
Consensus routing maintains consistency by separating safety and liveness
It makes routing predictable and possibly securable
We can have an Internet that has high availability!

## Slide 17: Beautiful Idea!
Food for thought:
  Did this paper impact academic research?
    (Yes!)
  Did this paper impact practice?
    (Only indirectly – we’ll come back to this)
Notes: We’ll return to these questions momentarily

## Slide 18: What’s wrong with Internet routing?
Full-mesh iBGP doesn’t scale
  # sessions, control traffic, router memory/cpu
  Route-reflectors help by introducing hierarchy
    but introduce configuration complexity, protocol oscillations/loops
Hard to manage
  Many highly configurable mechanisms
  Difficult to model effects of configuration changes
  Hard to diagnose when things go wrong
Hard to evolve
  Hard to provide new services, improve upon protocols

## Slide 19: Routing Control Platform
What’s causing these problems?
  Each router has limited visibility of IGP and BGP
  No central point of control/observation
  Resource limitations on legacy routers
network
RCP
Solution: compute routes from central point, remove protocols from routers
network
network
RCP
Inter-AS Protocol
RCP
Notes: Why drawing RCP above network boxes – just say orally, that it’s not part of the forawarind plane

## Slide 20: RCP in a single ISP
Better scalability: reduces load on routers
Easier management: configuration from a single point
Easier evolvability: freedom from router software
RCP
iBGP
Notes: Then bring up 3 points after describe slide (Animate)
On this slide – say what it is that y’uouve impelemntede, this is an imprlmentation that emultates full mesh, empasisze per router decision making - very important piont to bring up!!! Say why is not just a route reflector.
Put text on slide to say why arrows going in both directions, available routes up and assigned routes down.
Reduce number of routers, just show some on maybe just internal ones send up igp. Maybe just say gets igp, and take out lines to internal routers.

## Slide 21: Principle 1
Compute Routes Using Consistent State

## Slide 22: Example of a Forwarding Loop
RR1
RR2
C1
C2
3
3
1
1
1
d
C1 learns BGP route to destination from RR1
C2 learns BGP route to destination from RR2
C1 sends packets to RR1 via its IGP shortest path which traverses C2
Persistent forwarding loop 
C2 sends packets to RR2 via its IGP shortest path which traverses C1

## Slide 23: Path Computation on Consistent View
RCP learns all externally learned routes
Computes consistent router-level paths
Benefits:
  Intrinsic loop freedom and faster convergence
  RCP does not have to stick to BGP decision process
    Can “pin” paths for traffic engineering and other purposes
RR1
RR2
C1
C2
3
3
1
1
1
d
“RR2”
“RR2”
RCP

## Slide 24: Principle 2
(Centrally) Control Routing Protocol Interaction

## Slide 25: BGP-IGP Interaction
d
11
10
A
B
C
BGP route selection process uses IGP costs to tie-break between equally good egress points
  If multiple egress points, choose the one with shortest IGP path (known as “hot potato” routing)
Once egress-point is selected, BGP relies on IGP to reach the egress point
d
9
10
A
B
C
Path cost change due to
failure, traffic engineering
or maintenance

## Slide 26: Principle 3
Support Flexible, Expressive Policies

## Slide 27: Centralized Configuration
RCP implements policies for entire AS
  Knows about sessions to all other ASes
  Implements policies in terms of relationship with Ases
    Today’s router configuration cannot capture this
Benefits
  Simpler configuration
  Do not have to tag routes with state
Sprint
UUNet
A
C
10.0.0.1
192.168.0.1
RCP

## Slide 28: Interdomain RCP: All ASes have RCPs
Before: RCP gets all eBGP routes from neighbors
iBGP
eBGP
After: ASes exchange routes via RCP
RCP
AS 3
AS 2
AS 1
iBGP
Physical
peering
Inter-AS Protocol
RCP
RCP
RCP

## Slide 29: Practical Challenges
Scalability
  Decision elements responsible for many routers
Reliability
  Surviving failures of decision elements and routers
Consistency
  Ensuring multiple decision elements behave consistently
Security
  Network vulnerable to attacks on decision elements
Interoperability
  Legacy routers and neighboring domains
Response time
  Delays between decision elements and routers
Notes: The paper outlines a bunch of future work

## Slide 30: ONIX (OSDI’10 Paper)
Distributed coordination
  Integrated with ZooKeeper
  Useful for leader election, locking, barriers, etc.
Scalability
  Partition: different tasks, switches, or parts of the NIB,
  Aggregate: combine statistics and topology information
Reliability
  Network failures: application’s responsibility
  Reachability to ONIX: reliable protocol, multipath, etc.
  ONIX failure: distributed coordination amongst replicas

## Slide 31: Consistent Updates
Abstractions for Consistent Updates [HotNet’11, SIGCOMM’12]
Fabric [HotSDN’11]
LOUP [HotNets’12]
…

## Slide 32: Yet!
Almost none of this literature sprung directly from RCP!
Why?
  One theory: Multi-domain is way too hard. (Start with single domain!)
Notes: Rather, it came out of SDN (Martin Casado et al.)

## Slide 33: My issues with this paper
“Using standard distributed systems protocols”
“Overlay networks lack direct control over IP-layer”

## Slide 34: My issues with this paper (2)
Emphasized “enabling innovation”
But anything that can be accomplished with a centralized solution can also be accomplished with distributed protocols
Notes: Some of you may have heard me make this same complaint

## Slide 35: Close Call
“routing protocol functionality should be separated from the routers”
Yet the paper (correctly) doesn’t do away with IGP
Intra-domain routing protocols work very well
    Provably self-stabilizing
    React to failures quickly
    Already widely supported

## Slide 36: Prediction
Changing inter-domain routing is hard
Yet,
I predict upcoming work on wide-area SDN*
  *based on discussions with Ethan Katz-Bassett

## Slide 37: Prediction
SDN provides a centralized view that you can optimize over, coordinate with, and reason about
Recent systems give better visibility and control into other ASes and how their routing affects traffic the origin’s traffic (WhyHigh, RevTR, Lifeguard, etc.)
Flatter Internet, more direct peering more paths to choose from

## Slide 38: Prediction
ISPs are run pretty poorly in general
Google (in particular) depends on the availability of other ISPs, and they have a huge incentive ($$) to improve availability
They want to: (a) understand the impact of routing changes, (b) exert (or give) more control over ISP’s routing decisions without doing thing that would mess up Google’s traffic

## Slide 39: Prediction
A huge portion of traffic now comes from a small number of CDNs. This means:
  Paths are now content eyeball (no intermediate ASes)
  Caches bytes out >> bytes across backbone
  slight changes to request routing cause HUGE changes in eyeball traffic
  TE changes in this world (lots more control, also worse consequences of screwing up)