## Slide 1
The Click Modular Router
Robert Morris, Eddie Kohler, John Jannotti, Frans Kaashoek (MIT), 1999
Presented by Colin Scott

## Slide 2
Motivation
Overview
Discussion
Outline

## Slide 3
Router Software
  Is expected to do much more than routing (firewall, prioritize, classify differentiated services, tunnel, filter, perform NAT), and the expectations are growing
  Is not flexible or extensible. Designs are monolithic, closed, and static
   A new application model is needed
Motivation

## Slide 4
Solution - Click Modular Router
Underlying Idea: Programmable Routing
  View a router as a directed graph of elements
  Packets move from element to element
  Extensions simply require the addition/transposition of elements
  Three new concepts:
    Pull processing
    Flow based router context
    Explicit queues

## Slide 5
The Architecture
Elements:
  Building blocks – Each represents a single router function
  Overall functionality determined by connecting a group of elements into a graph
Input and Output ports:
  Every element has one or more input and output ports
  Ports can be push, pull, or agnostic
  Connections must match: pull to pull, push to push, or either to agnostic
Configuration strings:
  Initialize the per-element state, customize element behavior

## Slide 6
An example:
IP router

## Slide 7
The Architecture..Continued
Push and Pull processing
  Certain tasks are better suited to one or the other, e.g.
    Packet schedulers are easily expressed using pull inputs
    Packet processing best implemented as a series of push elements
  A queue is a push to pull converter

## Slide 8
The Architecture..Continued
Flow based router context
The topology graph can be queried as to what elements are downstream,upstream, etc..
Filters can be passed to stop processing (e.g., “return all downstream elements up until queues”)
Best example use is RED – examine the total downstream queue length for congestion estimation

## Slide 9
The Architecture..Continued
Explicit Queues
  Click elements do not have implicit queues on their input and output ports
  Queues are explicit elements
  This enables valuable configurations that are difficult to arrange otherwise, e.g.
    a single queue feeding multiple interfaces,
    a queue feeding a traffic shaper on the way to an interface
  Important for performance

## Slide 10
Router extensions
Differentiated Services
Classification, tagging, shaping, dropping, queuing, and scheduling functions.
Rate-limiting elements
Best effort delivery

## Slide 11
Results on a Linux setup
73000 packets/sec – 90% as fast as Linux IP

## Slide 12
Similar Systems
x-kernel
  Composing network protocols in a layered fashion
  “Session” nodes
Scout
  Path-oriented processing
  Implicit queues
Unix System V Streams
  Imprecise control over queuing, scheduling
XORP
  Modularize the control plane – inspired by Click
Focused on end-nodes, where information flow is vertical
(device to user), rather than horizontal (device to device)

## Slide 13
Discussion
Did Click influence the way we think about routing software?
Who’s “we”?
Academia?
Industry?

## Slide 14
Discussion
What made Click influential?
[ Eddie Kohler’s thoughts ]

## Slide 15
Discussion
Why hasn’t Industry adopted Click?
Software routers aren’t fast enough
  Forwarding handled by specialized hardware on the NIC itself
Legacy code
Lack of incentives

## Slide 16
Discussion
Many types of I/O handling would benefit from
modular design, not just packet forwarding
Video streaming
Web requests
Handling terminal input
Etc.

## Slide 17
An aside: The evolution of router software
Early routers were essentially general purpose computers
Today, high-performance routers resemble supercomputers • Exploit parallelism • Specialized hardware components
• Until 1980s (1st generation): standard computer • Early 1990s (2nd generation): delegate to interfaces -- switching fabric • Late 1990s (3rd generation): distributed architecture • Today: distributed over multiple racks

## Slide 18
Limitations
Lack of explicit support for inter-node communication
Connections are governed by packet-flow. Implementing shared elements or communication that is not part of the packet flow, e.g. routing tables, is difficult.
Didn’t figure out how to schedule CPU time amongst competing push and pull paths

## Slide 19
One goal is to go back and see how the authors thought of the work at the time they wrote the paper, versus how we think about the work today. What are the characteristics of papers that turn out to be important?